## Slide 1
Depth to water source
Pressure of outlet

## Slide 2
Depth to water source
Pressure of outlet
Energy required ~ f(depth to water,
pressure of outlet,
amount of water moved)

## Slide 3
Let’s say this pump requires 3 units of energy for this task.

## Slide 4
Say the pump uses diesel.

## Slide 5
Say the pump uses diesel.
One unit of diesel contains 3 units of energy.

## Slide 6
Say the pump uses diesel.
One unit of diesel contains 3 units of energy.
FTM does this math, and says you need 1 unit of diesel (which is used for CO2 calcs). They also report your energy use as
3 units.

## Slide 7
Methodology | Energy use | Diesel use
FTM | 3 units | 1 unit

## Slide 8
Say the pump uses diesel.
However, diesel fuel only converts 30% of it’s energy into work (thermal efficiency). The rest is lost as heat, etc.

## Slide 9
Say the pump uses diesel.
You will therefore actually need 3 units of diesel to run the pump.

## Slide 10
Say the pump uses diesel.
You will therefore actually need 3 units of diesel to run the pump.
This translates to needing 9 units of energy for this pump, when you are using diesel to power it.

## Slide 11
Methodology | Energy use | Diesel use
FTM | 3 units | 1 unit
NRCS1 | 9 units | 3 units
1https://ipat.sc.egov.usda.gov/Default.aspx

## Slide 12
Different energy sources have different energy contents and efficiencies
Diesel contains the most energy per unit, and is 30% efficient.
Gasoline contains less energy per unit, and is only 25% efficient.
Electricity contains a small amount of energy per unit, but is 90% efficient.

## Slide 13
Field to Market references this table, but does not use it in its calculations.

## Slide 14
The energy used for irrigation should be responsive to the source of energy used.